## Slide 1: Router & Switch
SILLA UNIVERSITY
컴퓨터 소프트웨어공학부
노철우 교수

## Slide 2: Cisco CLI
Router>en
Router#config t
Router(config)#hostname R1
R1(config)# no ip domain-lookup
R1(config)# enable secret cisco
R1(config)# banner motd #Welcome cisco!!! #
R1(config)# line con 0
R1(config-line)# exec-timeout 0 0
R1(config-line)# password cisco
R1(config-line)# logging synchronous
R1(config-line)# login
R1(config-line)#exit
R1(config)# line vty 0 4
R1(config-line)# exec-timeout 0 0
R1(config-line)# password cisco
R1(config-line)# login
R1(config-line)#exit

## Slide 3: Cisco CLI
R1(config)# int g0/0/0
R1(config-if)# ip add 172.16.3.1 255.255.255.0
R1(config-if)# no sh
R1(config-if)# exit
R1(config)# int s0/0/1
R1(config-if)# ip add 172.16.2.1 255.255.255.252
R1(config-if)# clock rate 64000
R1(config-if)# ^Z
R1#

## Slide 4: Cisco CLI
R1# sh ip int br
R1# sh ip route

## Slide 6
WAN port: 8,9
LAN port: 0-7
800M Router

## Slide 8: 800M 라우터
telnet
conf t
  hostname R1
  line vty 0 4
  pass cisco
  transport input telnet
  login
  exit
enable secret cisco

## Slide 9: 800M 라우터
1. Router LAN port
conf t
int vlan 1
ip add 172.30.1.1 255.255.255.0
no sh
int g0/2 // PC 연결 port
switchport mode access
switchport access vlan
no sh
2. Router WAN port
int g0/8 //WAN
ip add 172.30.2.1 255.255.255.0
no sh

## Slide 10: 800M 라우터
router rip
ver 2
network 172.30.0.0

## Slide 11: Router & Switch

## Slide 12: Router
conf t
vlan 192
int vlan 192
  ip add 192.168.1.1 255.255.255.0
  no sh
ip default-gateway 10.10.10.1
int fa0/9
    swithport mode access
    switchport access vlan 192
no ip split-horizon

## Slide 13
port 할당
  # int range fa0/1-5
  #sw mode trunk
  #sw trunk native vlan 99
  # int range fa0/6-10
  #sw mode access vlan 30
VLAN 생성
  #vlan 99
  #name management
관리 인터페이스 주소 할당
  #int vlan 99
  #ip add 172.17.99.11 255.255.255.0
  #no shutdown

## Slide 14: Router
conf t
vlan 192
int vlan 192
  ip add 192.168.1.1 255.255.255.0
  no sh
  ip rip send ver 2
  ip rip recv ver 2

## Slide 15: switch 2 -vlan
conf t
ip routing
int vlan 192
  ip add 192.168.1.10
  ip rip send ver 2
  ip rip recv ver 2
  no sh
int g 1/0/2
  switchport mode access
  switchport access vlan 192
  no sh

## Slide 16: switch 2 -vlan
conf t
ip routing
int vlan 192
  ip add 192.168.1.10
  ip rip send ver 2
  ip rip recv ver 2
  no sh
int g 1/0/2
  switchport mode access
  switchport access vlan 192
  no sh

## Slide 17: Inter-VLAN routing
(config)# vlan 1
(config)# vlan 2
(config)# int vlan 1
(config-if)# ip add 1.1.1.1 255.255.255.0
(config-if)# no sh
(config-if)# int vlan 2
(config-if)# ip add 2.2.2.2 255.255.255.0
(config-if)# no sh
(config-if)# int g0/1
(config-if)# switchport acc vlan 1
(config-if)# int g0/2
(config-if)# switchport acc vlan 2

## Slide 18: inter-vlan
config)# int vlan 99
(config-if)# ip add 10.10.10.10 255.255.255.0
(config-if)# no sh
(config-if)# exit
(config)# ip default-gateway 10.10.10.1
(config)# int range g0/6, g0/2
(config-if)# sw m tr
(config-if)# sw tr native vlan 99
(config-if)# no sh
# sh int trunk
# sh int status
# sh int g0/2 switchport

## Slide 19: switch
switch(config)#interface ethernet 12-16
switch(config-if)#switchport trunk allowed vlan 15,20-22,40,75
switch(config-if)# switchport trunk allowed vlan add 100-120
switch(config)#interface ethernet 10
switch(config-if)#switchport trunk native vlan 12
switch(config)# show interface switchport
switch>show interfaces trunk

## Slide 20: switch encapsulation
===========
SWITCH(config)# int g0/3
(config-if)# sw tr encapsulation dot1q
(config-if)# sw m tr
(config)# int g0/4
(config-if)# sw tr allowed vlan all
(config-if)# sw tr allowed vlan remove 4
스위치의 default gateway를 라우터로 설정해준다.
SWITCH(config)# ip default-gateway 192.168.10.1
Routerconfig-if)# int g0/1.10
Routerconfig-subif)# encapsulation dot1q 10
Router(config-subif)#ip address 192.168.10.1 255.255.255.0
PC: gateway - 라우터 서브인터페이스 주소

## Slide 21: SP
bridge priority
  conf t
  spanning-tree vlan 200 priority 32768

## Slide 22: 800M 라우터
username silla priviliege 15 password 0 cisco
username comeng priviliege 15 password 0 cisco
conf t
login local, no login local
transport input telent/ssh
exit
conf t
vlan 173
int vlan 173
ip add 172.16.3.1 255.255.255.0
int g0/9
-switchport mode access
-switchport access vlan 173

## Slide 23: 800M 라우터
=============
pass recovery
1.ctl break
rommon 1. config-reg 0x
copy

## Slide 24: 재분배
router rip
redistribute eigrp 1 metric 2
=다른 프로토콜을 RIP/EIGRP으로 재분배시 초기 메트릭 지정해야함
router eigrp 1
redistribute ospf 1 metric 1000 1 1 1 1500
router ospf 1
redistribute eigrp 1 subnets metric-type 1/2 (E1/E2)
redistribute connected subnets